Finite Impulse Response
Digital Signal Processor
By Vijay Nayar
madric@gmail.com
https://github.com/vnayar/fir_dsp

---
Finite Impulse Response
- A filter whose impulse response is of finite duration.
- May use delayed inputs as feedback.
- Digital systems use discrete time.
  - e.g. y[n] = 0.5*x[n] – 1.5*x[n-1] + 0.7*x[n-2]
- General Form:
y[n] = sum from i=0 to N c[i] * x[n - i]

---
Delay Function
c(x) = (x == -5) ? 1 : 0

---
Noise Reduction
c(x) = normal(x)

---
Low Pass Filter
c(x) = sin(x)/x

---
Computation Overview
New data input x[n] is written to memory.
  - e.g. input read from Analog to Digital Converter
1. Compute next output y[n] using summation.
2. Move y[n] to memory.
3. Output y[n] is read from memory.
  - e.g. output sent to Digital to Analog Converter
- Performance is critical!

---
Memory Model:
Circular Buffer
- One edit per write
- Fixed address range
- Easier for DMA
Memory / Address	Stored / Value
20040	0.8	x[n-1]
20041	1.0	x[n]
20042	0.2	x[n-4]
20043	0.4	x[n-3]
20044	0.6	x[n-2]
Memory / Address	Stored / Value
20040	0.8	x[n-2]
20041	1.0	x[n-1]
20042	1.2	x[n]
20043	0.4	x[n-4]
20044	0.6	x[n-3]
Newest
Oldest
Newest
Oldest

---
FIR Computation
Steven W. Smith, The Scientist and Engineer's Guide to Digital Signal Processing
http://www.dspguide.com/ch28/2.htm
1. Obtain a sample with the ADC; generate an interrupt
2. Detect and manage the interrupt
3. Move the sample into the input signal's circular buffer
4. Update the pointer for the input signal's circular buffer
5. Zero the accumulator
6. Control the loop through each of the coefficients
7. Fetch the coefficient from the coefficient's circular buffer
8. Update the pointer for the coefficient's circular buffer
9. Fetch the sample from the input signal's circular buffer
10. Update the pointer for the input signal's circular buffer
11. Multiply the coefficient by the sample
12. Add the product to the accumulator
13. Move the output sample (accumulator) to a holding buffer
14. Move the output sample from the holding buffer to the DAC

---
How to Squeeze Performance
- Stateful hardware components that can be programmed with behavior
- Components act in parallel
- Assembly supports parallel instructions
  - Read input sample & coefficient
  - Circular buffer support
  - Multiply & accumulate
  - Loop iteration

---
Hardware Overview

---
Assembly Language
1. r12 = _y; /* i12 points to beginning of y[ ] */
2. i4 = _x; /* i4 points to beginning of x[ ] */
3. dm1(cb0) = {i4, X_LENGTH, SIGN, NUMBER_SIZE} /* Initialize DAG1 */
4. dm2(cb0) = {i12, Y_LENGTH, SIGN, NUMBER_SIZE} /* Initialize DAG2 */
5. /* prime the registers */
6. f2 = dm1(cb0), f4 = dm2(cb0)
7. f8 = f2*f4, f2 = dm1(cb0), f4 = dm2(cb0);
8. loop 20, 1; /* loop 20 times over the next 1 instruction */
9. /* highly efficient main loop */
10. f12 = f8 + f12, f8 = f2*f4, f2 = dm1(cb0), f4 = dm2(cb0);
11. f12 = f8 + f12, f8 = f2*f4; /* complete the last loop */
12. f12 = f8 + f12;
13. dm2(_result) = f12; /* store the result in memory */
Main data path
designed
around this.

---
Assembly Language Format
Parallel Instructions
- f12 = f8 + f12 ; f4 = d2(cb0) ; f8 = f2 * f4 ; f2 = d1(cb0)
  -- 22 bits -- -- 10 bits -- -- 22 bits -- -- 10 bits --
  Type A Type D Type A Type D
- Type (A)LU
  - 6-bit opcode, 4-bit reg-dest, 4-bit reg-srcA, 4-bit reg-srcB, 4-bit func
- Type (D)AG
  - 4-bit opcode, 4-big reg-dest/src, 2-bit cbs

---
Assembly Language Format
Loop Instructions
- loop iterations, size;
- -- 32-bit --
- Type (L)oop
- 6-bit opcode, 12-bit iter, 12-bit size
- Support a limited number of nested loops.

---
FIR DSP Top Level
4-Port Register Files
RF1 memory focus
RF2 arithmetic focus
64-bit instructions
32-bit registers
16-bit address space

---
VHDL vs. Verilog
Jinkies! I better call
Scoob and the gang
to solve this mystery!
- VHDL
  - Highly redundant
  - Error prone
  - Difficult to write tests
- Verilog
  - Concise and clear syntax
  - Flexible and powerful
  - Excellent testing capabilities

---
Program Sequencer
/**
 * Program Sequencer.
 * This module increments the program counter, and also applies loop
 * logic without the need for separate jump instructions every iteration.
 * Loop counters are stored internally and are initialized with a special
 * instruction once per loop.
 */
module prog_seq
  (
   input clk, reset,
   input we, // Write-enable for loop registers
   input [11:0] iter, size,
   output reg [15:0] addr);
   reg [3:0] stack_index;
   reg [15:0] loop_start[3:0];
   reg [15:0] loop_end[3:0];
   reg [11:0] loop_iter[3:0];
   always @(posedge clk, posedge reset) begin
      if (reset) begin
        addr <= 0;
        stack_index <= 0;
      end
      else if (we) begin
        stack_index = stack_index + 1;
        loop_start[stack_index] <= addr + 1;
        loop_end[stack_index] <= addr + 1 + size;
        loop_iter[stack_index] <= iter - 1;
        addr <= addr + 1;
      end

---
Program Sequencer 2:
The Revenge
      else begin
        if (addr == loop_end[stack_index]) begin
        if (loop_iter[stack_index] !== 0) begin
        loop_iter[stack_index] <= loop_iter[stack_index] - 1;
        addr <= loop_start[stack_index];
        end
        else begin
        stack_index <= stack_index - 1;
        addr <= addr + 1;
        end
        end
        else
        addr <= addr + 1;
      end // else: !if(we)
   end // always @ (posedge clk, posedge reset)
endmodule // prog_seq

---
Program Sequencer Unit Test
/**
 * Test - Program Sequencer
 * The Program Sequencer is responsible for moving simple loop logic to
 * hardware in a reduced number of clock cycles. This is another critical
 * component for the DSP and must be tested thoroughly.
 */
module test_prog_seq();
   reg clk, reset;
   reg we;
   reg [11:0] iter, size;
   wire [15:0] addr;
   // Instantiate the device-under-test (dut).
   prog_seq dut(clk, reset, we, iter, size, addr);
   // generate clock
   always begin
      clk = 0; #5;
      clk = 1; #5;
   end
   // Apply test inputs one at a time.
   initial begin
      // Reset the program sequencer.
      $display("Resetting the Program Sequencer.");
      reset = 1; we = 0; iter = 0; size = 0; #11;
      if (addr !== 0) $display("Initial addr check failed (%h).", addr);

---
Program Sequencer
Unit Test (cont.)
      // Check normal operation first.
      reset = 0; we = 0; iter = 0; size = 0; #10;
      if (addr !== 1) $display("Addr increment check failed (%h).", addr);
      // Initialize a loop.
      reset = 0; we = 1; iter = 2; size = 4; #10;
      if (addr !== 2) $display("Increment on loop init failed (%h).", addr);
      // Loop first instr at 0x02, last instr at 0x06.
      reset = 0; we=0; iter = 0; size = 0; #40;
      if (addr !== 6) $display("Last instruction not visited (%h).", addr);
      // See if we caught our jump.
      #10;
      if (addr !== 2) $display("Loop jump failed (%h).", addr);
      // Now see if this loop finishes.
      #50;
      if (addr !== 7) $display("Loop failed to terminate (%h).", addr);
      $display("Test complete.");
   end // initial begin
endmodule // test_dag

---
Data Address Generator
/**
 * Data Address Generator.
 * May be initialized to a range of memory, which will be managed as a circular
 * buffer. When written to, the base address, length, direction/sign, and
 * increment exponent are specified. When read, the address saved in the
 * internal address poiner is outputted. The internal pointer is then
 * incremented by 2^(exponent) when sign is 0, and decremented when sign is 1.
 * If the internal pointer exceeds the limits set by the base and length,
 * the address "wraps-around" to the other end of the circular buffer.
 */
module dag
  (
   input	clk,
   input	re, // Read-enable
   input [2:0]	cbs, // Circular Buffer Select
   input	we, // Write-enable
   input [15:0]	base, // These four inputs add to 32-bits.
   input [11:0]	len,
   input	sign,
   input [2:0]	expt,
   output reg [15:0] a); // Address
   reg [15:0]	cb_base[3:0];
   reg [15:0]	cb_top[3:0];
   reg [15:0]	cb_inc[3:0];
   reg [15:0] cb_ptr[3:0];

---
Data Address Generator (cont.)
   always @(posedge clk) begin
      if (we) begin
        a <= 16'bz;
        cb_base[cbs] <= base;
        cb_ptr[cbs] <= base;
        cb_top[cbs] <= base + {3'b0, len};
        cb_inc[cbs] = 1 << expt; // Blocking assignment
        cb_inc[cbs] = sign ? -cb_inc[cbs] : cb_inc[cbs];
      end
      else if (re) begin
        a <= cb_ptr[cbs];
        cb_ptr[cbs] = cb_ptr[cbs] + cb_inc[cbs]; // Blocking assignment
        cb_ptr[cbs] = cb_ptr[cbs] >= cb_top[cbs] ? cb_base[cbs] : cb_ptr[cbs];
        cb_ptr[cbs] = cb_ptr[cbs] < cb_base[cbs] ? cb_top[cbs] : cb_ptr[cbs];
      end
      else
        a <= 16'bz;
   end // always @ (posedge clk)
endmodule // dag

---
Data Address Generator Unit Test
/**
 * Test - Data Address Generator
 * The DAG is a complex and stateful component. Testing it for correctness
 * is essential before work can be built upon it.
 */
module test_dag();
   reg clk;
   reg re;
   reg [2:0] cbs;
   reg we;
   reg [15:0] base;
   reg [11:0] len;
   reg sign;
   reg [2:0] expt;
   wire [15:0] a;
   // Instantiate the device-under-test (dut).
   dag dut(clk, re, cbs, we, base, len, sign, expt, a);
   // generate clock
   always begin
      clk = 1; #5;
      clk = 0; #5;
   end
   // Apply test inputs one at a time.
   initial begin
      // Initialize a circular buffer.
      $display("Initializing Circular Buffer.");

---
Data Address Generator
Unit Test (cont.)
      // Start at address 0xAB00, buffer is 8 bytes, and each read
      // advances the pointer by 2^1 = 2 bytes.
      re = 0; cbs = 0; we = 1;
      base = 16'hAB00; len = 8; sign = 0; expt = 1; #11;
      // Read the first address.
      re = 1; we = 0; #10;
      if (a !== 'hAB00) $display("Read 1 failed (%h).", a);
      #10;
      if (a !== 'hAB02) $display("Read 2 failed (%h).", a);
      #10;
      if (a !== 'hAB04) $display("Read 3 failed (%h).", a);
      #10;
      if (a !== 'hAB06) $display("Read 4 failed (%h).", a);
      #10;
      if (a !== 'hAB00) $display("Read 5 (wrap) failed (%h).", a);
      $display("Test complete.");
   end // initial begin
endmodule // test_dag